## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 1-a, Spring 2016

## Slide 2: Today’s Topics
Syllabus review
Number systems
Conversion of a number from one base to another.
Operations in non-decimal system.
Boolean Algebra
Logic Operators
Logic gates

## Slide 3: Assignment for W1-b
Reading assignment: Chapter 1 (light reading).
Get the textbook ASAP.
Get your PC up running in good shape.
Visit Black Board Learner frequently.
STM32F3-Discovery kit and LCD panel are coming on 2/8/16. ($20.00 each)

## Slide 4: Various Number system
Example of base-10 (decimal) number system.
Example of base-5 number system.
Example of base-3 (ternary) number system.
Example of base-2 (binary) number system.
Notations of number systems
  Decimal : 0d987, 98710
  Binary: 0b1011, 1011b, 1011B, 10112,
  Hexadecimal: 0x00FF, 00FFH, 00FFh, 00FF16

## Slide 5: Binary and Hexadecimal Numbers
Decimal | Binary | Hexa-decimal | Decimal | Bianry | Hexa-decimal
0 | 0000 | 0 | 8 | 1000 | 8
1 | 0001 | 1 | 9 | 1001 | 9
2 | 0010 | 2 | 10 | 1010 | A
3 | 0011 | 3 | 11 | 1011 | B
4 | 0100 | 4 | 12 | 1100 | C
5 | 0101 | 5 | 13 | 1101 | D
6 | 0110 | 6 | 14 | 1110 | E
7 | 0111 | 7 | 15 | 1111 | F

## Slide 6: Conversions between different number systems (positive integers)
Decimal to non-decimal conversion
N10=a0*R**(n) +a1*R**(n-1) +a2*R**(n-2) +… an*R**0
Non-decimal to decimal conversion
  Consecutive division method
  Weight subtraction method in binary number system

## Slide 7: Exercise Problems
Convert 0xFF to decimal.
Convert 0x123 to a decimal.
Convert to hexadecimal and then to binary.
75710
35610

## Slide 8: Binary arithmetic operations
Arithmetic Operations are +, -, *, /.
Method 1: Convert to decimal numbers, compute and convert back to binary numbers.
Example: 1101(+,-,*,/)101=
Method 2: Operate directly in binary system. Maintain the concepts of carry and borrow in the same way of decimal arithmetic.
  Example: 1101(+,-,*,/)101=

## Slide 9: Exercise Problems
Add, subtract and multiply in binary.
1111 and 1010
Kilo (K), mega(M), Tera(T)
Mili(m), micro (u), nano (n)

## Slide 10: What is Logic ?
Logic is a mathematical disciple of arguing true of false of a statement.
A simple statement (Chris is a boy. The door is open.) is a variable of either true/false (or 1/0).
A logic statement has a structure of “if A (is true/false), then B (is true/false) (If-Then statement)”. (B<-A, or simply B=A)

## Slide 11: Boolean Algebra
Basic operation: AND (.), OR(+), NOT(‘)
Each variable (A, B or X) is a simple statement . (The door is open. John is here.)
Note :X+X=X, X.X=X, X+1=1, X.X’=0, etc.
A truth table lists all possible input instances and corresponding outputs in a table form.
Factoring and multiplying-out work in the same way as arithmetic operation.
X.(Y+Z)=X.Y+X.Z
Note that X+(Y.Z)=(X+Y).(X+Z) is also true always.
De Morgan’s Theorem
(X+Y)’=X’.Y’ (XY)’=X’+Y’

## Slide 12: Boolean (Logic) Operations
Logic operations of AND, OR, NOT may compound to NAND, NOR and XOR.
Be careful to distinguish arithmetic operations (+, .) from logic operations (AND(.), OR(+)). Even “=“ has different meanings in Boolean operations.
When variables (ex. x,y,z) have values (true(1), false(0)) and are connected by AND operator, the expression looks like a binary number (ex. 101). But it is not.

## Slide 13: Logic Gates
A gate is a device that performs a basic operation. (AND gate, OR gate, NOT gate)
Gates come in all different characteristics (speed, logic levels) and prices.