## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 1-b, Spring 2016

## Slide 2: Review of Week 1-a
Review of various Number systems
  Conversion between number systems
  Basic numeric (arithmetic) operations
Review of Logic
  What is logic?
  What are the variables of a logic statement?
  IT statement
  Boolean operations

## Slide 3: Today’s topics
Micro-processor vs. Micro-controller (MCU)
Segmentation of MCU industry
ARM Cortex-M4(3.2)

## Slide 4: Assignment for Week 1-c
Reading assignment: Chapter 3
Download STM32F303xx Datasheet and browse it. (light reading)
STM32F3-Discovery Board is on its way.

## Slide 5: Announcement
From: Hsu, Chuen Sent: Monday, January 25, 2016 4:32 PM To: Subject: Collecting transcripts for prerequisite check
Everyone:
Please be reminded to collect student transcripts (with course prerequisites highlighted or circled) for verifying prerequisites by Friday (1/30). Also, please remind students that those have not turn in transcripts will be disenrolled from classes starting next week.
Thank you!
Dick

## Slide 6: Glossary
ARM: Advanced RISC Machine, or Ashton Raggatt McDougall
Bus: Fixed pathway of data or signals. A bus has single or multiple lines. The number of lines of a bus is called the width of the bus. Ex. Power bus, ground bus, data bus, instruction bus etc.
CPU: central processing unit
Micro-processor: CPU on a single chip
MCU: micro controller unit (CPU+Peripherals)
MPU: memory protection unit
I/O: input/output
IP: intellectual property
SoS/SoC: System on silicon/system on chip

## Slide 7: Micro-processor
(Computer) Processor is a central unit of a compute which executes instructions. It is also called a CPU (central processing unit)
Computers have evolved from a building size to a floor size, to a file cabinet size (mini-computer) to a desktop size (micro-computer)
The size of a processor evolved accordingly. A processor in a micro-computer is micro-processor.
A general purpose micro-processor has only CPU and basic RAM inside. All peripheral devices (ROM, I/O ports, etc.) are external.
Micro-processors are versatile, fast and expensive.

## Slide 8: History of microprocessor
The first microprocessor was made by Intel. It was a 4-bit processor, a technological marvel at that time. Today, a super computer has 128 bit processor.
CISC (Complex Instruction Set Computer) vs. RISC (Reduced Instruction Set Computer)
  Two different design philosophy in architecture.
  RISC claims that a small instruction set simplifies architecture, thus more efficient.
  Today CISC (ex. Intel) has also adapted to RISC concept. The distinction is blurry.

## Slide 9: Microcontroller
A (single-chip) micro-controller has all functional blocks (CPU + peripherals) fabricated on a single a chip.
Micro-controllers are simple to use, cheap but function specific.
A system with a micro-controller built in is called an embedded system. A microcontroller functions as an embedded element of the system. (examples, printer, TV remote controller, toys, etc.)

## Slide 10: Typical Layout of MCU
Fig 1.2 (p5)

## Slide 11: Triangle of MCU industry
MCU Design House
Semiconductor Manufacturing
Software Development Support

## Slide 12: Segmentation of MCU industry
Today, a microprocessor design company separates itself from manufacturing. Manufacturing again separates itself from software support (IDE). An IDE company works closely with design companies and manufacturing companies.
This separation of processor design companies (ARM, etc) from manufacturing companies (STM, TI etc.) from IDE companies (Keil, GNU etc.) makes the industry practice very competitive.
Each manufacturing company adds his own flavor in terms of functions and prices in order to out-perform his competitors in the market.
Implementation variations- performance (speed, tolerance) and price factors, bipolar to CMOS

## Slide 13: Licensees of ARM Cortex-M4
ST Microelectronics
Texas Instrument
NXP (Philips)
Atmel
OKI
etc, etc.
The list changes in time dynamically .

## Slide 14: ARM Cortex-M4
ARM is a name of the company who designs processors and license them to manufacturers. (ARM is an acronym)
Cotex-M4 is one processor design of ARMv7 architecture generation.
A processor architecture determines the instruction set (ISA).
Refer to Figure 1.5 on p18.

## Slide 15: Cortex-M4 Instruction set
Cortex-M4 is a 32-bit processor.
Many instructions do not need 32 bits. Hence making all instructions in 32 bits is a waste.
Cortex-M4 has Thumb-2 instruction set which has both 16-bit and 32-bit instructions.
The reason that the width of a bus is critical is more because of the complex circuitry that companies each bus line, not the line itself.

## Slide 16: Performance of Cortex M4
3 stage pipeline for instruction fetch.
Multiple buses for high speed throughput (AMBA)
Thumb 2 instruction set (16 bit instructions and 32 bit instructions work together without any switching overhead.)
NVIC (Nested Vector Interrupt Control) handling
Low power management

## Slide 17: Applications of Cortex-M4
Low-cost microcontroller: high-end toys
Automotive: Real time control. ABS
Data communications: Blue tooth applications
Industrial control: Robot control
Consumer products
And many others