## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 2-a, Spring 2016

## Slide 2: Review of Week1-c
STM32F303 Layout
  Processor
    Core
    Core peripherals
  System peripherals
    External I/O ports
    Internal I/O ports
  Buses
  Memory blocks and registers

## Slide 3: Today’s Topics
Processor core architecture (4.1~4.2)
Major components of a core
  Program counter
  Instruction register
  Instruction decoder
  ALU
  Core Registers
  Special registers

## Slide 4: Assignments
Reading assignment: Chapter 4.3-4.4

## Slide 5: SSTM32F303 Layout
Processor
  Core
  Core peripherals
Buses
System peripherals
  External I/O ports
  Internal I/O ports (functional blocks)
Memory blocks
STM32F303xC Datasheet (DM00058181) P12

## Slide 6: Core Structure
Program Counter (PC)
Instruction Register (IR)
Instruction Decoder
Special Registers
ALU
ROM
(Instruction Code)
RAM
(Data)
Register Bank
***Remember this diagram***
Instruction Bus
Control Bus
Data Bus
Core

## Slide 7: 5 Major Components of a core
Program Counter (PC)
Instruction register
Instruction decoder
Register bank (SRAM)
ALU

## Slide 8: Register Bank
A register is a memory array of 32 bits.
A register is made of SRAM and is designed for easy and fast access of data.
A register has a name (R0, R1 etc.) but no address.
A collection of 16 registers is called a register bank. (R0~R15)
Designated function registers
  R13: Stack pointer (SP)
  R14:The link register (LR)
  R15: The program counter (PC)

## Slide 9: Program Counter (PC)
PC contains the address of the next instruction to be executed.
PC holds an address, not an instruction code.
PC is updated right after the next instruction is fetched and stored in IR (instruction register).
PC is R15 in the register bank.

## Slide 10: Instruction Register (IR)
Instruction register (IR) holds the currently executing instruction code.
IR feeds the instruction to the instruction decoder.

## Slide 11: Instruction decoder
Instruction decoder decodes the instruction into a series of micro-codes and feeds the control bus.
This series of micro-codes operates and executes the instruction in multiple clock cycles.
The design of the instruction decoder is highly protected

## Slide 12: ALU
The Arithmetic and Logical Unit (ALU) performs arithmetic operations (+,-, *,/) and logic operations (AND, OR, NOT, shift).
ADD R2, R0, R1 (R2=R0+R1)
SUB Rd, Rn, Rm (Rd=Rn-Rm)
AND Rd, Rn (Rd=Rd&Rn)
ALU symbol
In Cortex M4, ALU cannot be read directly.

## Slide 13: Special (Function) Registers
Special (function) registers perform only very specific functions only
Special registers in Cortex-M4
  Program Status registers
  Interrupt Mask registers
  Control register: will be discussed later.
  FPU registers: will be discussed later.
Special registers are accessible by special instructions only.
  MSR: Move from general register to special register.
  MRS: Move from special register to general register.

## Slide 14: Program Status Registers
PSR is also called PSW (program status word).
Cortex M4 processor has three program status registers (APSR, IPSR and EPSR). APSR has the most significance for application. (Ch 4.3/Ch 3.2.1)
APSR holds the flags (N,Z,C,V,Q) which indicate the status of ALU.
  N: negative
  Z: zero
  C: carry/borrow
  V: overflow
  Q saturation
An instruction has S-suffix to set PSR flags.
ADDS R0, R1, R2