## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 2-b, Spring, 2016

## Slide 2: Review of Week-2a
Processor core architecture (4.1~4.3)
Major components of a core
  Program counter
  Instruction register
  Instruction decoder
  ALU
  Core Registers
  Special registers

## Slide 3: Today’s Topics
Core bus architecture (-)
Sequence of instruction execution (-)
Pipeline (-)
Reset and reset sequence (4.8)

## Slide 4: Assignments
Reading assignment: Chapter 4.5, 4.8

## Slide 5: Core Bus Architecture
A bus is a data/signal highway of internal communication.
Ex. Power bus, ground bus, data bus, address bus
Bus architecture determines the efficiency and limitation of a core.
The core adopts Harvard architecture internally for efficiency.
External of a core has Von Neumann (Princeton) architecture for simplicity.

## Slide 6: Harvard vs. Princeton
In Harvard architecture, the instruction code memory (usually ROM) and the data memory (SRAM) are connected to two different buses (I-bus, D-bus). This architecture allows simultaneous operation of instruction and data.
In Von Neumann (Princeton) architecture, the code memory and the data memory share the same bus. Von Neumann architecture is adopted outside of the core.

## Slide 7: Sequence of instruction execution
The program counter (PC, R15) contains the address of the current instruction code.
  Fetch an Instruction code from the code ROM designated by PC. Then load it at the instruction register (IR). Then increment PC.
  Decode the instruction code into micro-codes.
  Execute a series of actions such as read /write a register, shift ALU, transfer data from one address to another, etc.
Then the core repeats this “fetch-decode-execute” cycle.

## Slide 8: Pipeline
The Cortex-M4 processor has a three-stage pipeline.
With pipeline, PC fetches the next instruction in anticipation before execution completes.
When this anticipation fails (ex. Branch), the pipeline has to flush and start over.

## Slide 9: Cortex M4 Memory Map
Figure 4.31, P114
Memory means ROM, RAM and peripheral I/O registers. Not core registers.

## Slide 10: Reset Sequence
Cold start (bootstrapping, or booting in short) triggers the reset process.
0X00 of the ROM has the value of SP (R13). It tells where the stack is located.
0X04 of the ROM has the vector (address) of the reset interrupt. This is the address of the very first instruction to execute.
Note that ROM and RAM are outside of the core. The core treats them with address, not with name.