## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 3-a, Spring, 2016

## Slide 2: Review of Week-2c
Interrupt service and exception handlers (4.5)
  NVIC
  Interrupt Service Routine (ISR)
  Vector Table
Reset sequence (4.8)
Modes of operation (4.2.1)

## Slide 3: Today’s Topics
What is Assembler language?
Types of Assembler codes.
Groups of Assembler codes.
Instruction codes to transfer data.

## Slide 4: Assignments
Reading assignment: Chapter 5
  Skip any discussion on ftp (floating point) or mask(PRIMASK etc.)
  Skip 5.6.6 (data conversion)
  Skip 5.6.7 (bit-field operation)
  Skip 5.6.10 (saturation operation) and after.
Alumni visit next class.

## Slide 5: What is Assembly language?
Low level language
HLL(High level language) codes are compiled to assembly codes before execution.
Assembler assembles, links and loads.
Codes written in assembly are small and fast.
Assembly code is closely related to the core architecture (ISA) and machine specific.
Coretex-M4 uses Thumb-2 instruction set. 16-bit codes and 32-bit codes are executed by one instruction decoder.

## Slide 6: Types of Assembly codes
Directive- An instruction to the assembler. These are not translated to machine codes (non-executable).
  The beginning of the program: AREA
  The end of the program: END
  Others: ALIGN, EQU, DCD, SPACE, etc.
A macro code is expanded to multiple executable codes during assembling time.
An executable code is translated to a machine code one-to-one.

## Slide 7: Assembly codes by function
Date transfer instructions
  Core register to Core register
  Core register to memory
Date operation instructions
  Arithmetic operations
  Logic operations
Flow-control instructions
  Unconditional branching
  Conditional branching

## Slide 8: Assembly Code Template
;Date 2-1-2016
;by John Smith
;This program demonstrates the basic template of assembly.
;Colored words are reserved.
area myprogram, code, readonly
entry
export __main ;two underbars.
__main b start
; This space is reserved for EQU assignments
start nop ;replace nop with an executable code.
nop
b start ;main stays in the loop.
end ;end of the program, not execution.

## Slide 9: Assembly codes
Assembly language is case sensitive. Type all in upper or lower case. Labels may be mixed.
A label starts at the 1st column of a line, nothing else. Do not put anything at the 1st column if it is not a label.
; is the beginning of a comment. Each comment line starts with ;

## Slide 10: Data Transfer instructions Core register to core register
mov rd, rs ;rd: destination, rs: source.
mov r2, r0 ;move (copy) the data in r0 to r2.
mov rd, #number ;assign rd with #number
;The number should be less than 256 (1 byte).
mov r0, #0x12
mvn rd, rs ;move 1’s compliment of rs to rd
mvn ro, r1
neg R1, R2 ;move 2’s comp to R1.

## Slide 11: Data Transfer instructions Core register to core register
movw rd, #number ;assign the lower 16-bits ; of rd with the number.
movw r0, #0x1234
movt rd, #number ; assign the upper 16-bits ; of rd with the number.
movt r0, #0x5678

## Slide 12: Data Transfer instructions Core register to memory
Memory is outside of the core. It includes ROM, RAM and peripheral I/O registers.
Memory data is referred to by an address.
ldr rd, [rs] ;load rs with the data located at the address in rs. Rs contains the address of the memory.
ldr rd, =number ;load rd with the 32-bit number.
ldr r1, =0x20001000
ldr r0, [r1] ;load r0 with the data at 0x20001000.

## Slide 13: Data Transfer instructions Core register to memory
str rs, [rd] ;store the data in rs to the address in rd.
;Note that the 1st operand is the source.
ldr r1, =0x20001004
str r0, [r1];store the data in r0 to 0x20001004
Example
    LDR R0, =0x20000FF0
    LDR R1, =0x0000AAAA
    STR R1, [R0]

## Slide 14: Data Transfer instructions Register to Stack memory
Stack is a designated area in SRAM. A stack pointer (SP, R13) points to the end of the stack.
push {rn} ;put the data in rn to the stack ;and decrement SP by 4.
pop {rn} ;put the data at SP to Rn
;and increment SP by 4.
Note {} symbols around a register.
rn may be a list of registers.
{r1, r2, r3} {r1-r4} {r1, r2-r4, r5}

## Slide 15: Example
You cannot move from mem to mem directly.
Then how to move the data in one address to the other address?
  LDR R0, =0X20000FF0
  STR R1, [R0]
  LDR R0, =0X20000FF4
  LDR R1, [R0]