## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 3-b, Spring, 2016

## Slide 2: Review of Week-3a
What is Assembler language?
Types of Assembler codes.
Groups of Assembler codes.
Instruction codes to move data.

## Slide 3: Today’s Topics
Addressing modes
Arithmetic operation
Logic operation
Shift and rotate operation
Suffices in Cortex-M4

## Slide 4: Assignments
Reading assignment: Chapter 5
  Skip any discussion on ftp (floating point) or mask(PRIMASK etc.)
  Skip 5.6.6 (data conversion)
  Skip 5.6.7 (bit-field operation)
  Skip 5.6.10 (saturation operation) and after.
Install Keil uVision on your computer.
Homework 1 assignment.
Quiz 1 when?

## Slide 5: Addressing methods
direct addressing
MOV R1, R2 ; move r2 to r1.
2) immediate addressing
MOV R1, #3 ; assign 310 to R1 register.
3) indirect addressing
LDR R1, [RN]
  [RN]: The memory data at the address which is stored at RN.
  ***MOV does not take indirect addressing.
4) Offset indirect addressing
LDR R1, [RN, OFFSET]

## Slide 6: Offset indirect addressing
Offset Indirect addressing
LDR R1, [RN, OFFSET]
    The data located at [RN+OFFSET] is moved to R1.
    RN does not change.
Pre-indexed indirect addressing
LDR R1, [RN, OFFSET]!
    The data located at [RN+OFFSET] is moved to R1.
    Then RN is updated to RN+OFFSET.
Post-indexed addressing
LDR R1, [RN], OFFSET
    The data located at [RN] is moved to R1.
    Then RN is updated to RN+OFFSET.

## Slide 7: Arithmetic operations
Arithmetic instruction has three operands.
ADD R0, R0, R1 ; R0=R0+R1
ADD R0, R1, #12 ;R0=R1+12
ADC R0, R1, R2 ;R0=R1+R2+Carry
SUB R0, R1, R2 ; R0=R1-R2
SUB R0, R1, #12 ;R0=R1-12
UMUL RdLo, RdHi, Rm, Rs ;RdHi/RdLo=Rm*Rs

## Slide 8: Core Structure
Program Counter (PC)
Instruction Register (IR)
Instruction Decoder
Special Registers
ALU
ROM
(Instruction Code)
RAM
(Data)
Register Bank
***Remember this diagram***
Instruction Bus
Control Bus
Data Bus
Core

## Slide 9: Example of addition
LDR R0, =0X00000FFF
LDR R1, =0X00000AAA
ADD R3, R0, R1

## Slide 10: Processing Date (Logic)
Logic operations are bit-wise.
AND R1, R2, #immed ;R1=R2 & immed
ORR R1, R2, #immed ;R1=R2|immed
EOR R1, R2, #immed ;R1=R2||immed
BIC R9, R8, #0XFF00 ; Clear [15:8] ->R9.
Example
LDR R2, =0X05050505
EOR R1, R2, #0XFFFFFFFF
What is in R1?

## Slide 11: Shift/Rotate instructions
Logical shift feeds 0 (zero) at the end bit.
  LSR R0, R1, #4 ;Logical shift right by 4 bits
  LSL R0, R1, #4 ; Logical shift left by 4 bits
Arithmetic shift feeds itself at the end bit.
  ASR R0, R1, #4 ;arithmetic shift right by 4 bits
Rotate
ROR R0, R1, #4 ;Rotate R1 ->R0 by 4 bits
ROL
RRX R0, R1, #4 ; Rotate R1 including C ->R1 by 4 bits

## Slide 12: Example of shift instruction
LDR R1, =0XAAAAAAAA
LOOP
LSR R1, R1, #2
B LOOP
Set a breakpoint at LSR line and repeat step over several times. Expand xPSR for detail.
Replace LSR with other shift instructions, and do the same thing.
        B

## Slide 13: Example of multiplication
Compute m1*0x000f. m1 is 16 bit long and is located at 0x20001000.
  equ m1addr 0x20001000
  ldr r5, =m1addr
  ldr r1, [r5] ;load r1 with m1
  mov r0, #00 ;clear r0
  add r0, r0, r1 ;add m1 to r0
  lsl r1, r1, #1 ;multiply m1 by 2
  add r0, r0, r1 ;add 2*m1 to r0
  lsl r1, r1, #1 ;multiply m1 by 4
  add r0, r0, r1 ;add 4*m1 to r0
  lsl r1, r1, #1 ;multiply m1 by 8
  add r0, r0, r1 ;add 8*m1 to r0

## Slide 14: Cortex M4 code suffices
S ;Sets APSR after execution
  Without S, APSR is not set except for several instructions such as cmp. Next class topic.
  ADD R0, R1, R2 ;APSR is not set
  ADDS R0, R1, R2 ;APSR is set
W,H, B ; Word, half-word or byte operation
  ADDH R0, R1, R2
Conditional suffices ;next class topic