## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 4-a, Spring, 2016

## Slide 2: Review of Week-3b
Addressing modes
Arithmetic operation
Logic operation
Shift and rotate operation
Suffices in Cortex-M4

## Slide 3: Today’s Topics
Unconditional branching
  Branching with no return
  Branching with return
Conditional branching
  Conditions
  Conditional executions
  Compare and test
  IT instruction

## Slide 4: Assignments
Reading assignment: Chapter 5
  Skip any discussion on ftp (floating point) or mask(PRIMASK etc.)
  Skip 5.6.6 (data conversion)
  Skip 5.6.7 (bit-field operation)
  Skip 5.6.10 (saturation operation) and after.
Quiz 1 on 2/27 (Fri)
Homework 1 due on 2/28 (Sun)

## Slide 5: Homework 1
Assignment
Due
Discussion

## Slide 6: Operation of uVison
Successful Blinky
How to create a .s file?
How to remove or add an existing .s file?
How to build a .s file?
How to start a debugger and download an object file?
How to set a breakpoint and why?
How to run a program on the board?

## Slide 7: Unconditional branch
Branch with no return
  B Label ; Branch to Label. One word.
  BX Rm ;Branch to the address in Rm. 2 words.
Branch with return
  BL Label ;Branch and link to Label.
  ; Subroutine call to Label.
  ;BL stores the return address
  ;to Link Register (LR, R14).
  ;How to return back from a subroutine?
  BLX Rm ;Subroutine call to the address in Rm.

## Slide 8: Subroutine call
….
bl routine1
….
…..
routine1
…..
……
bx lr ;return to lr (link register) value.

## Slide 9: Conditional Branching
Conditional branching is done by one of the three codes.
  Execution code<condition>
  BEQ label ;Branch to Label if 0.
  Compare and test
CBZ R0, label
  It <condition> ;(If-then statement)
  IT EQ
  MOVEQ R0, R1

## Slide 10: Conditiond in Coretex M4
<condition> is the condition of xPSR.
  EQ Equal to zero
  NE Not equal to zero
  PL Positive
  MI Minus. Negative
  GT Greater than
  LT Less than
  GE Greater than or equal
  LE Less than or equal
There are many other conditions beside these.

## Slide 11: Conditional execution instruction
Add {condition} suffix to a executable code.
  LSLEQ R0, R0, #24 ;LSL if 0.
  ADDEQ R0, R0, #2 ;ADD if 0.

## Slide 12: Compare and Test (and Branch)
This is a register test, not a flag bit test in PSR.
CBZ Rm, Label
;Compare (test) Rm and branch to Label if zero.
CBNZ Rm, Label
; Compare (test) Rm and branch to Label if not zero.
CMP Rn, Rm
;Calculate Rn-Rm, and set flags. No branching.
TST Rn, Rm
;Rn AND Rm, and set flags. No branching

## Slide 13: IT Conditional Execution
If-Then statement
IT{x}{y}{z} <condition>
; where x, y, z are either T (then) or E(else).
  If condition met, then execute the 2nd line. Else not.
  If condition met, then execute the 3rd line. Else not.
  If condition met, then execute the 4th line. Else not.
  Each line should have a matching condition suffix.
IT statement maintains the pipeline without flushing, thus saves execution time.

## Slide 14: IT Statement Examples
IT EQ ;Add if zero, else nothing.
ADDEQ R0, R0, R1
ITTE NE ; If NE, execute the next 2 lines.
; If EQ, execute the 3rd line.
ADDNE R0, R0, R1
ADDNE R0, R0, R3
ADDEQ R2, R4, #1

## Slide 15: Example codes
A) mov r0, #5
Loop add r1, r1, #3
sub r0, r0, #1
cbnz r0, loop ;compare an branch if not zero.
exitloop . . ..
B) ldr r0, =0x00aa0000
Loop sub r0, r0, #1
cbnz r0, loop
exitloop . . .

## Slide 16: Instruction code summary
Data transfer | mov, mvn, neg, ldr, str, push, pop
Arithmetic | add, adc, sub, umul,
Logic | and, orr, bic, eor, asr, lsl, lsr, ror, rol, rrx
Branching | b, bx, bl, blx, it, cmp, cbz, cbnz
Suffix | (eq, ne, gt, lt, ge, le, mi, pl),(s, b, h, w)

## Slide 17: Looping in Assembly
LDR R0, =1
LDR R1,n
TOP CMP R1,#0
BEQ DONE
MUL R0, R0, R1
SUB R1,R1,#1
  B TOP
DONE STR R0, FACT
//compute n!
int k, fact, n;
fact=1;
for (k=n; k !=0; k--)
{
fact *=k;
}

## Slide 18: How to write an assembly program?
Generate an algorithm and draw a flowchart.
List required inputs, outputs, internal variables.
Allocate addresses to those variables.
Start coding in pieces, not a whole program.
Test each piece of codes, and debug the codes.
When all pieces proven all right, put them together to make a whole. Then test again.