## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 4-b, Spring, 2016

## Slide 2: Review of Week-4b
Unconditional branching
  Branching with no return
  Branching with return
Conditional branching
  Conditions
  Conditional executions
  Compare and test
  IT instruction

## Slide 3: Today’s Topics
Barrel shifter (5.8)
EQU
NOP
Assembly coding exercises

## Slide 4: Announcement
Reading assignment: Chapter 6.
Rgt LCD panel for the Discovery Kit.
Quiz 1 on 2/26 (Fri)
Homework 1 due on 2/28(Sun)

## Slide 5: Instruction code summary
Data transfer | mov, mvn, neg, ldr, str, push, pop
Arithmetic | add, adc, sub, umul,
Logic | and, orr, bic, eor, asr, lsl, lsr, ror, rol, rrx
Branching | b, bx, bl, blx, it, cmp, cbz, cbnz
Suffix | (eq, ne, gt, lt, ge, le, mi, pl),(s, b, h, w)

## Slide 6: Barrel Shifter
A barrel shifter is a hardware circuit which enables multiple bit shifting in one machine cycle.
op_code rd, rn, rm, shift_op #n
;It acts as if a compound instruction,
shift_op rm, rm, #n
op_code rd, rn, rm
Examples
add r0, r1, r2, asr #4
ldr rd, [rn, rm, lsl #n]

## Slide 7: EQU
EQU is a directive which is executed during assembly.
label equ constant
The label is replaced by the constant during assembly.
my_student_id equ 0x12345678
ldr r0, =my_student_id
Remember that a label starts at column 1.

## Slide 8: NOP (no operation)
NOP is a convenient code filler.
It takes one instruction cycle.
..
mov r1, #255
delay nop
sub r1, r1, #1
beq delay
..
..

## Slide 9: Assembly coding exercises
Exercise 1
Exercise 2