## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 5b, Fall, 2015

## Slide 2: Review W5-a
Assembly coding exercise
Memory map
Memory and peripherals
Refer to STM32F3 Data sheet. (posted on BB)

## Slide 3: Today’s Topics
Endians
Memory alignment
Quiz 1 preview

## Slide 4: Assignments
Reading assignment: Chapter 6.
Skip 6.7.4, 6.8-6.12
Quiz 1 on 2/26 (Fri)
Homework 1 due on 2/28(Sun)

## Slide 5: Endians
Little endian has LSB at bit[0].
Big endian has MSB at bit[0].
Default is little endian.
Endianess of the system can be changed but only at reset.
In default mode, ARM Cortext M4 is in the little endian mode.

## Slide 6: Memory Alignment
A word address has an ending bits of [00], i.e. multiples of 4.
A half word has an address of ending bit [0], i.e. multiples of 2.
ARM architecture allows unaligned memory for better compact storage.
But unaligned memory is slow in process.
Some instructions (stack, bit band operations) require aligned memory.
align is a directive to enforce memory alignment.