## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 5c, Spring 2016

## Slide 2: Review W5-b
Endians
Memory alignment
Quiz 1 preview

## Slide 3: Today’s Topics
Bit-band operation
Quiz 1

## Slide 4: Announcement
Reading assignment: Reference Manual-RM0316 Ver. 6
<http://www.st.com/web/en/resource/technical/document/reference_manual/DM00043574.pdf>
Homework 1 due on 2/28(Sun)

## Slide 5: Homework-1 Discussion
Project folder and the source code.
SRAM window

## Slide 6: Bit Band Operation
Cortex allows direct bit access in two memory regions (1MB each) by bit band operation.
  SRAM 0x2000 0000~0x200F FFFF
  Peripheral 0x4000 0000~0x400F FFFF
Each region has a alias region.
  SRAM 0x2200 0000~0x23FF FFFF
  Peripheral 0x4200 0000~0x43FF FFFF
Each bit in the bit-band region has a matching LSB bit of a word in the alias region.
Ex. 0x2000 0000 bit[0] => 0x2200 0000 bit[0]
  0x2000 2000 bit[2]=>0x2200 0008 bit[0]

## Slide 7: Read-Modify-Write Operation
You can read/write a LSB bit only in the bit-band alias region. (bit-band operation)
When a code writes on the alias region, actual operation occurs in the band region in a single sequence of read-modify-write.
A Bit-band operation is a single operation. Thus it cannot be broken (i.e. atomized).This operation is done by hardware (micro-codes).

## Slide 9: Advantages of Bit Band -1
Bit operation with less codes.
  Without bit band
    LDR R0, =0x20000000 ;Set up address
    LDR R1, [R0] ;Read
    ORR R1, #0x4 ;Modify. Set bit[2]
    STR R1, [R0] ;Store back
  With Bit band
    LDR R0, =0x2200 0008 ;Set up address
    MOV R1, #1 ;Set up data
    STR R1, [R0] ;Write on the alias.

## Slide 10: Advantages of Bit band-2
Boolean data storage is possible.
Bit band operation is a single operation. Read/modify/write operation is locked (atomized), and cannot be broken by multitasking or system exception.
Refer to Fig 6.12~6.15 (p212~215)