## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 6b, Spring 2016

## Slide 2: Review W6-a
Code exercise – bcc, movt, bne, rrx, bl, bx
Lab work #2
STM32F3 Discovery kit
STM32F303 VC device GPIO port

## Slide 3: Today’s Topics
Quiz 1 review
Homework 1 review
RCC configuration
GPIO registers
Lab Work #1 Announcement

## Slide 4: Announcements
Reading Assignment
  STM32F3 Reference manual (V.6)
  Chapter 9 Reset and Clock Control (RCC)
  Chapter 11 General Purpose I/Os (GPIO)
Lab work 1 announcement

## Slide 5: Bit writing techniques
LDR instruction to set bits R0[15:8]
  Example: ldr r0, =0x00005500
ORR instruction
  What if R0[31:16] and R0[7:0] have valid bits?
  LDR R3, =0x00005500 ;set a pattern
  ORR R0, R3, R0 ;ORR the pattern to R0
BIC and BFC instructions
  What if R0[15:8] has non-zero bits?
  Clear R0[15:7] with BIC or BFC instruction.

## Slide 6: RCC (Reset and Clock Control) port
RCC is an internal peripheral I/O. It is not connected to any pins.
All peripheral I/O are disabled (disconnected from CPU) at reset.
RCC does,
  Resets the system
  Controls internal/external clocks
  Connect/disconnect a peripheral to CPU by enable/disable the bus clock to the peripheral.
Unless RCC sets a particular I/O peripheral, the core cannot access the peripheral registers of the I/O.

## Slide 7: RCC configuration
RCC has total 13 (peripheral) registers.
Out of these, RCC_AHBENR controls AHB peripheral devices.
GPIO’s are AHB devices.
RCC base address is 0x40021000.
RCC_AHBENR has offset of 0x14
GPIO_F~A are set by bit [22:17]

## Slide 8: RCC_AHBENR register

## Slide 9: RCC configuration example
; Configure GPIO_E port (LED port)
RCC_BASE EQU 0x40021000
AHBENR_OFFSET EQU 0x14
AHBENR_GPIOEEN EQU 0x0200000 ;bit[21]
LDR R0, =RCC_BASE ; load base address for RCC
LDR R1, =AHBENR_OFFSET ; load offset for AHBENR
LDR R2, =AHBENR_GPIOEEN ; load GPIOE enable
LDR R3, [R0, R1] ; Read current AHBENR value
ORR R2, R2, R3 ; Modify AHBENR value to enable E
STR R2, [R0, R1] ; Write new AHBENR value to register

## Slide 10: GPIO Peripheral Registers
A GPIO port has 16 pins.
Each pin of a GPIO operates in either an input mode or output mode or alternate-function (AF) mode. ModeR (mode register) sets the mode of each pin. (00:input, 01:output, 10:AF )
In an output mode, the processor sends a data to ODR (output data register, 16 bit) Then the internal circuitry places this data to the port pins.
In an input mode, a signal at the port pin is stored at IDR (input data register, 16 bit). Then the processor reads this data.
GPIO is AF0 (Alternate function).

## Slide 11: GPIO Register Addresses
GPIOA Base Address 0x4800 0000
GPIOE Base Address 0x4800 1000
GPIO_ModeR Offset 0x00
GPIO_IDR Offset 0x10
GPIO_ODR Offset 0x14

## Slide 12: GPIOE ModeR

## Slide 13: Two steps of GPIO port operation
Step I: Configure the port registers.
    Set the base address and offset addresses
    Set ModeR.
Step II
  If output port, write a data to ODR.
  If input port, read the data in IDR.