## Slide 1: EECE237 Introduction to Embedded System
Sukgi Choi, Ph.D.
Week 6c, Spring 2016

## Slide 2: Review W6-b
Quiz 1 review
Homework 1 review
RCC configuration
GPIO registers
Lab Work #1 Announcement

## Slide 3: Today’s Topics
Lab 1 discussion
Template-Class configuration subroutine
GPIO coding
Bit writing techniques

## Slide 4: Announcements
Reading Assignment : STM32F3 Reference manual
  Chapter 9
  Chapter 11
Lab 1 due on 3/13.
Quiz #2 on 3/11 (Fri). (RCC, GPIO & TIM3)
Midterm on 3/25 (Fri).

## Slide 5: Q & A
ST-Link connection problem.
Use run, not single step in Debug mode.

## Slide 6: Configuring GPIOE for Output
GPIOE_BASE EQU 0X48001000
MODER_OFFSET EQU 0x00
IDR_OFFSET EQU 0x10
ODR_OFFSET EQU 0x14
; Configure GPIO_E as output port (LED port)
LDR R0, =GPIOE_BASE ;
LDR R1, =0x55550000 ; make all upper byte pins output.
STR R1, [R0, #MODER_OFFSET] ;STORE MODER=0X10
; Light up all LED’s
LDR R2, =0x0000 FF00
STR R2, [R0, #ODR_OFFSET]

## Slide 7: Configuring GPIOA for Input
GPIOA_BASE EQU 0X48000000
; Configure GPIO_A Pin [0] as input for the Push button
LDR R0, =GPIOA_BASE ;
LDR R1, [R0, #MODER_OFFSET] ;Make PA[0] input pin
BIC R1, R1, #0X03 ;reset only bit[1:0]
STR R1, [R0, #MODER_OFFSET] ;Bit[0] pin is an input
; Read the push-button
WAIT
LDR R1, [R0, #IDR_OFFSET] ;read IDR
ANDS R1, R1, #01 ;check if bit[0] is set.
BEQ WAIT ; If not pushed yet, wait till pushed.
next code ; The push button is pressed. Move on.

## Slide 8: LED_test.s program
; Structure the main program.
start
BL config_rcc ;configure RCC for GPIOA and GPIOE
BL config_gpioa ;Configure push-button port.
BL config_gpioe ;Configure LED port
main_loop
BL read_button ;R3=1 if the button is pressed.
CMP R3, #0
BLEQ LED_off
BLNE LED_on
B main_loop ;Stay in the infinite loop
;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;;

## Slide 9: Lab 1 Assignment
Student work
Study the template
Make changes in configuration when announced.
Change the starting number of the delay to make it 1 second delay.
Add codes to led_on_all, led-on_even and led_on_odd.

## Slide 13: Bit writing techniques
LDR instruction to set bits R0[15:8]
  Example: ldr r0, =0x00005500
ORR instruction
  What if R0[31:16] and R0[7:0] have valid bits?
  LDR R3, =0x00005500 ;set a pattern
  ORR R0, R3, R0 ;ORR the pattern to R0
BIC and BFC instructions
  What if R0[15:8] has non-zero bits?
  Clear R0[15:7] with BIC or BFC instruction.