## Slide 1: EECE237 Introduction to Embedded System Quiz 1 Study guide
Sukgi Choi, Ph.D.
Week 5-b, Spring, 2016

## Slide 2: Binary and Hexadecimal Numbers
Decimal | Binary | Hexa-decimal | Decimal | Bianry | Hexa-decimal
0 | 0000 | 0 | 8 | 1000 | 8
1 | 0001 | 1 | 9 | 1001 | 9
2 | 0010 | 2 | 10 | 1010 | A
3 | 0011 | 3 | 11 | 1011 | B
4 | 0100 | 4 | 12 | 1100 | C
5 | 0101 | 5 | 13 | 1101 | D
6 | 0110 | 6 | 14 | 1110 | E
7 | 0111 | 7 | 15 | 1111 | F

## Slide 3: Exercise Problems
Convert 0xFF to decimal.
Convert 0x123 to a decimal.
Convert to hexadecimal and then to binary.
75710
35610

## Slide 4: Glossary
Bus: Fixed pathway of data or signals. A bus has single or multiple lines. The number of lines of a bus is called the width of the bus. Ex. Power bus, ground bus, data bus, instruction bus etc.
CPU: central processing unit. The unit that executes instruction codes.
Micro-processor: CPU on a single chip
MCU: micro controller unit (CPU+Peripherals)
MPU: memory protection unit
I/O: input/output
Periphery: any circuit block outside of the processor.

## Slide 5: Micro-processor
(Computer) Processor is a central unit of a compute which executes instructions. It is also called a CPU (central processing unit)
Computers have evolved from a building size to a floor size to a file cabinet size (mini-computer) to a desktop size (micro-computer)
The size of a processor evolved accordingly. A processor in a micro-computer is a micro-processor.
A general purpose micro-processor has only CPU and basic RAM inside. All peripheral devices (ROM, I/O ports, etc.) are external.
Micro-processors are versatile, fast and expensive.
Microcontrollers are function specific and cheap.

## Slide 6: Microcontroller
A (single-chip) micro-controller has all functional blocks (CPU + peripherals) fabricated on a single a chip.
Micro-controllers are simple to use, cheap but function specific.
A system with a micro-controller built in is called an embedded system. A microcontroller functions as an embedded element of the system. (examples, printer, TV remote controller, toys, etc.)

## Slide 7: SSTM32F303 Layout
Processor
  Core
  Core peripherals
Memory blocks
System peripherals
  External I/O ports
  Internal I/O ports (functional blocks)
Buses
STM32F303xC Datasheet (DM00058181) P12

## Slide 8: Core Structure
Program Counter (PC)
Instruction Register (IR)
Instruction Decoder
Special Registers
ALU
ROM
(Instruction Code)
RAM
(Data)
Register Bank
***Remember this diagram***
Instruction Bus
Control Bus
Data Bus
Core

## Slide 9: Buses (STM)
STM uses AMBA (Advanced Microcontroller Bus Architecture) for bus structure.
The processor interacts with the system via 3 AHB (high speed) buses and 2 APB (low speed) buses.
High speed I/O’s (GPIO, DMA etc.) are connected to AHB buses. Low speed I/O’s (I2C, Timer, DAC etc.) are connected to APB buses.

## Slide 10: Register Bank
A register is a memory array of 32 bits.
A register is made of SRAM and is designed for easy and fast access of data.
A register has a name (R0, R1 etc.) but no address.
A collection of 16 registers is called a register bank. (R0~R15)
Designated function registers
  R13: Stack pointer (SP)
  R14: Link register (LR)
  R15: Program counter (PC)

## Slide 11: Program Counter (PC)
PC contains the address of the next instruction to be executed, assuming that instructions are executed sequentially.
PC holds an address, not an instruction code.
PC is updated right after the instruction is fetched and stored in IR (instruction register). Then PC is adjusted when necessary.
PC is R15 in the register bank.

## Slide 12: Instruction Register (IR)
Instruction register (IR) holds the currently executing instruction code.
IR feeds the instruction to the instruction decoder.

## Slide 13: Instruction decoder
Instruction decoder decodes the instruction into a series of micro-codes and feeds the control bus.
This series of micro-codes operates and executes the instruction in multiple clock cycles.
The design of the instruction decoder is proprietary and highly guarded.

## Slide 14: ALU
The Arithmetic and Logical Unit (ALU) performs arithmetic operations (+,-, *,/) and logic operations (AND, OR, NOT, shift).
ADD R2, R0, R1 (R2=R0+R1)
SUB Rd, Rn, Rm (Rd=Rn-Rm)
AND Rd, Rn (Rd=Rd&Rn)
ALU symbol
In Cortex M4, ALU cannot be read directly.

## Slide 15: Special (Function) Registers
Special (function) registers perform only very specific functions only
Special registers in Cortex-M4
  Program Status registers
  Interrupt Mask registers: will be discussed later.
  Control register: will be discussed later.
  FPU registers: will be discussed later.
Special registers are accessible by special instructions only.

## Slide 16: Program Status Registers
PSR is also called PSW (program status word).
Cortex M4 processor has three program status registers (APSR, IPSR and EPSR). APSR has the most significance for application. (Ch 4.3/Ch 3.2.1)
APSR holds the flags (N,Z,C,V,Q) which indicate the status of ALU.
  N: negative
  Z: zero
  C: carry/borrow
  V: overflow
  Q saturation
An instruction a S-suffix sets PSR flags at the end of execution.
ADDS R0, R1, R2

## Slide 17: Harvard vs. Princeton
In Harvard architecture, the instruction code memory (usually ROM) and the data memory (SRAM) are connected to two different buses (I-bus, D-bus). This architecture allows simultaneous operation of instruction and data.
In Von Neumann (Princeton) architecture, the code memory and the data memory share the same bus. Von Neumann architecture is adopted outside of the core.

## Slide 18: Sequence of instruction execution
The program counter (PC, R15) contains the address of the current instruction code.
  Fetch an Instruction code from the code ROM designated by PC. Then load it at the instruction register (IR). Then increment PC.
  Decode the instruction code into micro-codes.
  Execute a series of actions such as read /write a register, shift ALU, transfer data from one address to another, etc.
Then the core repeats this “fetch-decode-execute” cycle.

## Slide 19: Pipeline
The Cortex-M4 processor has a three-stage pipeline.
With pipeline, PC fetches the next instruction in anticipation before execution completes.
When this anticipation fails (ex. Branch), the pipeline has to flush and start over.

## Slide 20: Memory System
32 bit (4GB) address space of memory. This space is divided into 7 regions. The first two regions are the code (ROM) region and SRAM region.
  The starting address of the code region is 0x0000 0000
  The starting address of the SRAM region is 0x2000 0000.
Note that this memory space is outside of the core. In this space, each memory has an address.
Cortex-M4 supports both little endian and big endian systems. To be discussed later.
Bit Band Access allows atomic access to individual bits .
Memory Protection Unit (MPU) –to be discussed later.

## Slide 21: Cortex M4 Memory Map
Figure 4.31, P114
Memory means ROM, RAM and peripheral I/O registers. Not core registers.

## Slide 22: Stack and Stack Pointer (SP)
Memory is stored in a stack by word (4 bytes).
The Cortex stack has a full-descending stack operation model. The stack pointer (R13) keeps the address of the bottom of the stack (entry point) in Cortex.
A stack starts from a SRAM address (default 0x20008000)and ends at the address of the stack pointer (SP, R13).
Cortex has one stack, but two stack pointers.
  Main Stack Pointer (MSP)
  Process Stack Pointer (PSP)

## Slide 23: Stack Operation
The instructions to store and read data are POP are PUSH.
Descending stack
  Push adds data to the stack and decreases SP by 4.
  POP removes data from the stack and increases SP by 4.
  These changes in SP are automatic.
Example: POP {R0} PUSH {R1, R2-R5}

## Slide 24: Interrupt
A processor can respond to an input device in one of two ways.
  Polling: The processor checks the input/output device repeatedly until it is ready.
  Interrupt: The processor performs its routine (thread). When the input/output device is ready, it calls the processor’s attention (IRQ).

## Slide 25: The sequence of interrupt
The processor is running its own routine in thread.
An I/O source initiates an IRQ (interrupt request).
The processor halts the currently running program. All active data in the registers & memory are pushed to the stack. The stack pointer is adjusted.
The processor runs the Interrupt Service Routine (ISR). The start address of IRS is called a vector, and is stored in the vector table.
Once ISR is served (completed), the processor pops the previous data from the stack back to the registers & memory.
The processor resumes the previous thread.

## Slide 26: Exception and interrupt
When IRQ source is external to the processor, it is called an interrupt-push button, keyboard.
When IRQ source is internal in the processor, it is called an exception – fault, SysTick timer etc.
Exception is handled by a handler.
Interrupt is served by an ISR.
Other than this naming difference, they work in the same way.
Table 4.9(p105) illustrates the different exceptions.
Table 4.26(p108) illustrates corresponding vectors (ISR start addresses).

## Slide 27: Nested vectored Interrupts
If a processor receives a new IRQ while running ISR of a previous IRQ, it compares the priority of the new IRQ to that of the previous IRQ.
If the latter has a higher priority, the processor drops (interrupts) the currently running ISR, and runs a new ISR of the new IRQ.
If the latter has a lower priority, it is ignored until the higher IRQ’s are served.
This process of handling multiple IRQ’s with different priorities is called nesting.
When nested, each IRQ has a different starting ISR address (vector). Thus it is called nested vectored interrupt.

## Slide 28: Interrupt priority and masking
Cortex design can change the priority of an IRQ dynamically (on-the-fly). This applies to some IRQ’s but not all. (Ex. RESET)
A certain IRQ’s can be blocked (masked) from activation during the execution of a program. This is called interrupt masking. Masking is handled by interrupt mask registers (Special Registers).
Masking is useful for program development.

## Slide 29: Assembly codes by function
Date transfer instructions
  Core register to Core register
  Core register to memory
Date operation instructions
  Arithmetic operations
  Logic operations
Flow-control instructions
  Unconditional branching
  Conditional branching

## Slide 30: Addressing methods
direct addressing
MOV R1, R2 ; move r2 to r1.
2) immediate addressing
MOV R1, #3 ; assign 310 to R1 register.
3) indirect addressing
LDR R1, [RN]
  [RN]: The memory data at the address which is stored at RN.
  ***MOV does not take indirect addressing.
4) Offset indirect addressing
LDR R1, [RN, OFFSET]

## Slide 31: Offset indirect addressing
Offset Indirect addressing
LDR R1, [RN, OFFSET]
    The data located at [RN+OFFSET] is moved to R1.
    RN does not change.
Pre-indexed indirect addressing
LDR R1, [RN, OFFSET]!
    The data located at [RN+OFFSET] is moved to R1.
    Then RN is updated to RN+OFFSET.
Post-indexed addressing
LDR R1, [RN], OFFSET
    The data located at [RN] is moved to R1.
    Then RN is updated to RN+OFFSET.

## Slide 32: Unconditional branch
Branch with no return
  B Label ; Branch to Label. One word.
  BX Rm ;Branch to the address in Rm. 2 words.
Branch with return
  BL Label ;Branch and link to Label.
  ; Subroutine call to Label.
  ;BL stores the return address
  ;to Link Register (LR, R14).
  ;How to return back from a subroutine?
  BLX Rm ;Subroutine call to the address in Rm.

## Slide 33: Conditional Branching
Conditional branching is done by one of the three codes.
  Execution code<condition>
  BEQ label ;Branch to Label if 0.
  Compare and test
CBZ R0, label
  It <condition> ;(If-then statement)
  IT EQ
  MOVEQ R0, R1

## Slide 34: Conditiond in Coretex M4
<condition> is the condition of xPSR.
  EQ Equal to zero
  NE Not equal to zero
  PL Positive
  MI Minus. Negative
  GT Greater than
  LT Less than
  GE Greater than or equal
  LE Less than or equal
There are many other conditions beside these.

## Slide 35: Instruction code summary
Data transfer | mov, mvn, neg, ldr, str, push, pop
Arithmetic | add, adc, sub, umul,
Logic | and, orr, bic, eor, asr, lsl, lsr, ror, rol, rrx
Branching | b, bx, bl, blx, it, cmp, cbz, cbnz
Suffix | (eq, ne, gt, lt, ge, le, mi, pl),(s, b, h, w)

## Slide 36: Barrel Shifter
A barrel shifter is a hardware circuit which enables multiple bit shifting in one machine cycle.
op_code rd, rn, rm, shift_op #n
;It acts as if a compound instruction,
shift_op rm, rm, #n
op_code rd, rn, rm
Examples
add r0, r1, r2, asr #4
ldr rd, [rn, rm, lsl #n]

## Slide 37: Memory Mapping of peripheral region
The peripheral region starts from 0x4000 0000.
The region is divided into different I/O devices by bus. (ex. APB1 devices, AHB1 devices, etc.)